THE DATA LINK LAYER
frames are the data link layer PDUs
The data link layer moves bits across the link and can add reliability to the / raw communications link	The data link layer / usually adds both a header and trailer to the data presented by the network layer.
The frame header typically contains a source and destination address	“physical address”
and / some control information
The body of the frame / contains the sequence of bits being transferred across the network	The trailer usu- / ally contains information used in detecting bit errors / CRC cyclical redundancy / check
A maximum size is associated with the frame	because all systems must allocate memory space (buffers) for the / data. / In a networking context, a buffer is just special memory allocated for / communications
The data link layer performs framing, physical addressing, and error detection	the data link layer can perform some type of flow control / Flow / control makes sure senders do not overwhelm receivers