# Multiple Access Protocols in Computer Network
Data link layer is recponcible for cummunication between two nodes	If there is a dedicated link between the sender and the receiver then data link control layer is sufficient
Main Function are: / data link control / multiple access control	Data link control is recponcible for reliable transmission message over transmission channel / using tecknique like framing / error control and flow control
	Multiple access control / when multiple station can access transmission channel simulatnineus / multiple access control is required for reduce collision
Multiple access protocol: / random access protocoles / aloha / casma / aloha pure / csma cd / csma CA / controlled acces protocoles / reservation / token / polling
random access protocole / all the station have the same preority / anny station can send data depending on the medium state inactive or occupied / it has two features / 1- there is no fixed time for sending data / 2- there is no fixed sequence of station sending data	Random access protocole / all station have the same preiority / all sation can send or recive data depending of medium inactive or occupied / it has two features: / there is no fixed time for sending data / there is no fixed sequence of station sending data
	Aloha it was designed for wireless LAN / Aloha Pure / when station send data it will wait for ACK / if Ack does not com it will wait for random time / it call back off time and then re send data again, / since diferent station wait for different random time the probability of collision decrease / Aloha Slotted / its simmilair of aloha pure excepte we divide time into slots and the sending of data is allowed only in the beginning of this slots, / if station misse slots it wait for the next one / this reduce the propability of collision